## Slide 1: Cardiovascular magnetic resonance: basic principles and applications - an overview
Dr Sanjay Prasad MD MRCP
Consultant Cardiologist
Royal Brompton Hospital, London
National Heart & Lung Institute, Imperial College London

## Slide 2: Assessment of Function

## Slide 3: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 4: What is CMR
Siemens sonata 1.5T (Bo)
Liquid helium, superconducting coil, far less energy wastage, continuous uniform fled within ~ 50cm sphere at centre of bore
Require fast, high strength gradients for switching during acquisition, for CMR.
2 x 2 x 1.5m

## Slide 5: CMR of Coarctation of the Aorta
Babu-Narayan SV, Kilner. pJ, Gatzoulis MA>. Curr Cardiol Rep. 2003

## Slide 6: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 7: What is MRI ?
Magnetic resonance imaging (MRI) uses the body’s natural magnetic properties to produce detailed images from any part of the body.
For imaging purposes the hydrogen nucleus (a single proton) is used because of its abundance in water and fat.

## Slide 8: MR
Freedom from ionising radiation
Acquisition in any plane without the need for reformatting
Versatility of available physiological information
Clinical validation

## Slide 9: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 10: Physics
Proton can be likened to the
planet earth, spinning on its axis, with a north-south pole.
Behaves like a small bar magnet.
Under normal circumstances, these hydrogen proton “bar magnets” spin in the body with their axes
randomly aligned.

## Slide 11
Outside Magnetic Field
10-14 m
The body contains many millions of 1H nuclei or protons in water and fat based tissues

## Slide 12
Outside Magnetic Field
10-14 m
Each one is a tiny spinning charged particle which produces a magnetic moment
Randomly orientated

## Slide 13: Physics
When additional energy (in the form of a radiowave) is added to the magnetic field, the magnetic vector is deflected.
The radio wave frequency (RF) that causes the hydrogen nuclei to resonate is dependent on the strength of the magnetic field.

## Slide 14
MAGNET
B0
Inside Magnetic Field
Nuclei precess around the direction of the magnetic field at the resonant frequency

## Slide 15: Physics
When the body is placed in a strong magnetic field, such as an MRI scanner, the protons’ axes all line up.
This uniform alignment creates a magnetic vector oriented along the axis of the MRI scanner.
MRI scanners come in different field strengths, usually between 0.5 and 2.0 tesla.

## Slide 17: Physics
Most diseases manifest themselves by an
increase in water content, so MRI is a sensitive test for the detection of disease.

## Slide 18: Hydrogen Nucleus
Main active nucleus used in MR
Single proton (atomic number 1)
Used for MR:-
    Abundant in the human body (fat and water)
    Solitary proton so has a large magnetic moment

## Slide 19: Resonance and Signal Generation
Energy transition that occurs when an object is subjected to a frequency the same as its own
In MR resonance is induced by applying a radiofrequency (RF) pulse (excitation pulse)
    At the same frequency as the precessing hydrogen nuclei
    Or at 90° to magnetic field (Bo).

## Slide 20: Resonance
Hydrogen nuclei will resonante whereas other active nuclei do not because their gyromagnetic ratios are different to Hydrogen and so have different precessional frequency
Result
-energy absorption
-phase coherence

## Slide 21: Contrast
Difference in tissue characteristics
Fat – H atoms linked to Carbon
  Large molecules
  High inertia
  Low inherent energy
Water – small molecules with little inertia
  High rate of molecular motion
Differences in image contrast as different relaxation rates in each tissue

## Slide 22: Relaxation
Withdrawal of RF eneregy:-
  T1 recovery – exchange of energy from nuclei to their surrounding environment or lattice
  Fat has a high T1 signal
T2 Decay
  Exchange of energy from one nucleus to another
  High in fluids, lower in fat.

## Slide 23: Basic image generation
Different components of an MR system
Superconducting magnet  ALWAYS ON
Gradient coils
  Alter the magnetic field
  Responsible for the noise (rapid switching / current)
RF generator
  Energy to deflect the magnetisation
RF detector coils
  Within the table
  Surface coils
  Detect signal

## Slide 24: Basic image generation
H+ protons  tiny magnets  align with external magnetic field  spin (precess) at a frequency proportional to the magnetic field
‘LARMOR’ frequency f α Field strength
f ≈ 64MHz at 1.5T
 important for RESONANCE

## Slide 25: Basic image generation
Spinning protons  like tiny gyroscopes… 2 distinct properties:
Frequency
  cycles per second of spin
Phase
  orientation of net magnetisation vector
  IN PHASE = phase coherence OUT OF PHASE
  eg. If 2 protons start at the same position but one has a higher frequency, then they rotate at difference speeds and a difference in phase accumulates
Notes: Due to the difference in resonant frequency between water and fat, the protons may be misregistered by the Fourier transform.
Where fat and water appear together, this may be represented by a bright or a dark band at the fat/water interface.

## Slide 26: Basic image generation
RF energy  deflects net magnetisation temporarily
THEN… magnetisation returns to initial direction  ‘relaxation’  relaxation generates signal  image
Different tissue have different relaxation properties
Main magnetic field

## Slide 27: MR in a nutshell
Patient in magnetic field  protons align
Magnetisation disturbed by brief RF excitation pulse
Magnetisation allowed to return to equilibrium
  Relaxation  signal received
LOCALISATION of signals requires magnetic field gradients
Repeated many times (~128 – 256) to generate data needed
Data collected in a data space “k-space”
  k space is the collected data
  Fourier transform  creates image
‘k’ comes from the Fourier equation – k = 1/wavelength H(kx,ky) = h(x,y) cos(kxx + kyy)dx dy
∫
∞
-∞

## Slide 28: Basic image generation
RF  tips magnetisation into transverse plane
Magnetisation recovers into the longitudinal plane
  Two independent processes involved
T1 recovery
T2 decay

## Slide 29: Basic image generation
T1 recovery Recovery of longitudinal magnetisation

## Slide 30: Basic image generation
T2 decay Decay of transverse magnetisation  SIGNAL

## Slide 31: Basic image generation
T2 fast ~10-100ms
T1 slower ~500-1500ms
Different tissues have different T1/T2  images look different
Can manipulate image
sequence to bring out
desired contrast
ie. Tissues short / Fluids long
Gadolinium chelates
  Shorten T1  High signal
T2
T1
 | T1 (ms) | T2 (ms)
Fat | 250 | 60
Myocardium | 800 | 30
Liver | 575 | 50
Arterial blood | 1200 | 250
CSF | 2000 | 1000

## Slide 32: Basic image generation
SPATIAL LOCALISATION
  Need to identify the origin of a signal  image
GRADIENTS  Vary the magnetic field
  Frequency of protons varies linearly along the gradient
SLICE-SELECT
  Gradient in ‘z’ direction
  Precessional frequency varies along ‘z’ direction
  RF pulse of a certain frequency excites ONLY the protons at that frequency  slice ‘selected’
THICKNESS α
RF pulse bandwidth
Gradient field strength

## Slide 33: Basic image generation
After the slice has been selected…
  Need to know ‘x’ and ‘y’ coordinates
X-DIRECTION
  Gradient is applied  alters the frequency of the protons
  Different frequencies read out
  ‘FREQUENCY ENCODING’ or ‘READOUT’ gradient

## Slide 34: Basic image generation
After the slice has been selected…
  Need to know ‘x’ and ‘y’ coordinates
Y-DIRECTION
  Another gradient is applied for a short time
  This changes the frequency of the protons… hence they accumulate a phase shift
  Stronger gradient  greater phase shift
  ‘PHASE ENCODING’ needs to be repeated many times

## Slide 35: Basic image generation
All this data is acquired and stored
  ‘k-space’
To generate a full image
  Needs to be repeated multiple times
  Different ‘PHASE-ENCODING’ gradients

## Slide 36: K-space

## Slide 37: Speed and Turbo factors
Cardiovascular MRI demands fast imaging
Methods for speeding up acquisition needed
  MULTIPLE lines of data (echoes) per RF pulse
    SPIN ECHO  Use multiple 180º pulses
      Echo train length – ‘TURBO factor’ / TSE
    GRADIENT ECHO  Use multiple gradient reversals
      Echo planar imaging (EPI)
      Reduce the TR (repetition time)
  Reduce amount of data acquired
    Lower NPE - Rectangular Field of View
    Lower NPE – Lower spatial resolution
    Partial Fourier techniques – eg. HASTE
  PARALLEL IMAGING
    Use information from multiple coil elements – SENSE / SMASH

## Slide 38: CMR: Advantages
a wide range of soft tissue contrast provides the potential for the characterization of myocardial tissue.
Contrast among tissues depends on:-
proton (hydrogen nuclei) density
magnetic relaxation times of the protons
magnetic susceptibility effects.

## Slide 39: Magnetic Fields
Magnetic lines of flux
Number of lines per unit area =magnetic flux density
Units for measuring strength are
      Gauss
      Kilogauss
      Tesla

## Slide 40: Magnetic Field Strength
1 Tesla =10,000 Gauss
Earth -0.5 Gauss
Scanner -15,000-30,000 Gauss (1.5-3 T)

## Slide 41: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 42: Important MR System Components
RF Transmitter

## Slide 43: What is CMR
Siemens sonata 1.5T (Bo)
Liquid helium, superconducting coil, far less energy wastage, continuous uniform fled within ~ 50cm sphere at centre of bore
Require fast, high strength gradients for switching during acquisition, for CMR.
2 x 2 x 1.5m

## Slide 44
Surface receiver coils
Coil used to receive the signal from the cardiac region

## Slide 45
1.5 vs 3T
SNR
Cost
Sequences

## Slide 46: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 47: Evaluation
Function
Tagging
Diastolic function

## Slide 48: Myocardial Tissue Characterisation
Fat characterisation
    -ARVC
    T1-weighted spin-echo

## Slide 49: Myocardial Tissue Characterisation
Inflammation
  Myocarditis
  Sarcoidosis
  Recent infarct
T2-weighted spin-echo

## Slide 50: Myocardial Tissue Characterisation
Scar Tissue and Fibrosis
  Infarction
  IHD vs non-IHD Cardiomyopathy
  HCM
        Delayed Contrast-Enhancement

## Slide 51: GADOLINIUM-DTPA
Paramagnetic contrast agent
Reduces T1 relaxation time where taken up
Uptake into extracellular water and if cell membrane injured
Scar from infarction /fibrous tissue

## Slide 52: Contrast Enhancement in Infarction
TTC
MRI
Ex-vivo comparison of TTC and Gd-enhanced MR
R Judd, Northwestern University, Chicago

## Slide 53: Healthy Myocardium
LM myocardium: Red stain for glycogen

## Slide 54: Background: Scar Tissue
LM myocardium: Red stain for glycogen, in myolytic cytosol

## Slide 55: Late Enhancement

## Slide 56: Fibrosis

## Slide 57
Scar
Normal
Electron-micrograph, Bonow et al

## Slide 58: Where Are We?

## Slide 59
[Gd]
t
1-3min
10-20 min
<10s
1
2
3
Blood pool
Microvascular obs.
Isch
Normal
Infarcted
Kinetics of gadolinium: 3 time periods
1:First pass
2: Early
3: Late

## Slide 60: Viability - Transmural MI
Kim R, Judd R. Northwestern University, Chicago

## Slide 61: Viability
Kim R, Judd R. Northwestern University, Chicago

## Slide 62: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 63: CMR - Applications
Function
Anatomy
Perfusion
Flow
Viability
Angiography

## Slide 64: CMR Quantification
1
2
3
4
5
6
7
8
9
Base
Apex

## Slide 65: 3D Assessment of Ventricular Function
ES
ED

## Slide 66: Assessment of LV function
Multiplanar
No geometrical assumptions
Not limited by poor echo-window

## Slide 67: Early Detection of CAD
Glagov NEJM 1987; 316: 1371-5
The Glagov Phenomenon

## Slide 68: Spiral Coronary Wall CMR
Hu B, Meyer C. Stanford University

## Slide 69: Eccentric Plaque in LAD
X-ray angiogram
LAD
LV
RV
RVOT
LAD
Fayad ZA Circulation 2000
Notes: • X-ray angiogram from a 76 year-old male patient showing high-grade stenosis in the proximal left anterior descending coronary artery (LAD) (arrows, left panel). The in vivo cross-sectional black blood MR images of the LAD shows shows a large eccentric plaque with heterogeneous signal intensity (maximum thickness ~6mm). The heterogeneity may be due to the composition of the plaque.
• MR imaging is performed with a fast spin echo sequence with short ESP and long ETL imaging. Blood flow in the coronary artery lumen is suppressed with the velocity-selective inversion preparatory pulses and fat surrounding the coronaries is suppressed with an optimized chemical shift pulse. The slice thickness is 4 mm and the spatial resolution is 450 µm. LV represents left ventricle; RV represents right ventricle; RVOT represents right ventricular outflow tract.

## Slide 70: 3T Coronary CMR
Matthias Stuber, Beth Israel, Boston
RCA
LCx
RV
LV
Ao
PA
LMS
Ao
LAD

## Slide 71: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 72
Wrong TI

## Slide 73
Late Enhancement: Scanning too Early

## Slide 74: Overview
Basic Principles
Physics
Hardware
Range of sequences
Applications
Pitfalls
Safety concerns –devices/ contrast agents

## Slide 75: Safety
1.5 vs 3T
All stents are fine
All mechanical valves are fine at 3 months
Pacemakers
  No longer absolute but only under very tight conditions

## Slide 76: Contrast Agents
Evidence for nephrogenic systemic fibrosis
Incidence very low
Only seen in patients w ESRF (GFR<30)
Not seen w newer generation agents

## Slide 79: Conclusion
Wide range of applications
High resolution images
In-vivo tissue characterisation
Detailed information in 30 mins

## Slide 80
MR & CFD
Y. Xu et al., Imperial College
Carotid bifurcation wall shear