## Slide 1: Principles of Radionuclide Imaging
S Richard Underwood
MD FRCP FRCR FESC FACC FASNC
Professor of Cardiac Imaging
Imperial College London
and Royal Brompton Hospital

## Slide 2: Cardiac Imaging
 | Resolution | Speed | Contrast
X-ray | < 1mm | < 10ms | Low*
US | 1 – 3mm | 1 – 100ms | Moderate*
NM | 8 – 12mm | 5 – 10min | High
MR | 1mm | 30s – 5min | High
 | Anatomy | Function | Perfusion | Metabolism
X-ray | 4 | 4 | 1 | 0
US | 4 | 4 | 1 | 0
NM | 2 | 4 | 4 | 5
MR | 5 | 4 | 2 | 2

## Slide 3: Common abbreviations
RNI | Radionuclide imaging
MPI | Myocardial perfusion imaging
*MPS | *Myocardial perfusion scintigraphy
MUGA | Multi-gated acquisition
*RNV | *Radionuclide ventriculogram
RNA | Radionuclide angiocardiography
SPE(C)T | Single photon emission (computed) tomography
PET | Positron emission tomography
*C(X)T | *Computed (X-ray) tomography
*CMR | *Cardiovascular magnetic resonance
MRI | Magnetic resonance imaging
MRS | Magnetic resonance spectroscopy

## Slide 4: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 5: The Electro-Magnetic Spectrum

## Slide 6: Atomic structure

## Slide 7: Chemistry revision
Atomic number = protons
  defines an element
Atomic weight = protons + neutrons
  Defines an isotope or nuclide

## Slide 8: Radionuclides
Unstable isotopes or nuclides are called radioisotopes or radionuclides
Nuclear transitions lead to stable isotopes by several mechanisms, one of which leads to emission of a gamma ray
Electron transitions lead to emission of an X-ray

## Slide 9: Radioactive decay
Exponential decay is characterised by half-life
(the time for half of the radioactive nuclei in a sample to decay)
238U 4.5 x 109 years
14C 5730 years
226Ra 1600 years
131I 8 days
201Tl 72 hours
99mTc 6 hours
18F 2 hours
15O 2 minutes
Time
Radioactivity

## Slide 10: Positron emission

## Slide 11: Coincidence detection

## Slide 12: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 13: The Gamma Camera
Gamma rays are emitted from the radiopharmaceutical injected into the patient
Gamma rays pass through a collimator and strike a sodium iodide crystal, a scintillator which emits light when struck by gamma rays
Photomultiplier tubes convert the light to an electrical signal which is used to produce the image

## Slide 14: Gamma Camera
patient
positioning and summing circuits
NaI (Tl) detector
Collimator
Photomultiplier
tubes
Lead shielding
X coordinate pulse
Y coordinate pulse
VDU
energy
window
Z Pulse
Unblank
pulse
Discriminator
ADC
Processor

## Slide 16: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 17: Radiopharmaceuticals in Nuclear Cardiology
Single photon emitters |  | 
99mTc | erythrocytes, albumin | ventriculography
 | pyrophosphates | acute infarction
 | annexin-V | apoptosis
 | microspheres, MIBI, tetrofosmin | perfusion
201Tl | ionic | perfusion
195mAu | ionic | angiocardiography
111In | platelets | thrombus
 | white cells | infection
 | anti-myosin antibody | acute infarction, transplant rejection
67Ga | citrate | inflammation
81Kr | gos or solution | pulmonary ventilation, right ventriculography
131I | meta-iodo-benzylguanidine | sympathetic innervation
Positron emitters |  | 
11C | microspheres | perfusion
 | pyruvate, lactate, lactate, acetate, ß-methyl fatty acids, palmitate | metabolism
13N | ammonia | perfusion
 | glutamate | metabolism
15O | water | perfusion
18F | 2-fluoro-deoxyglucose | metabolism

## Slide 18: Myocardial perfusion tracers
Thallium
MIBI
Tetrofosmin

## Slide 19: Technetium-99m Generator
Mother radionuclide
  Molybdenum-99 on an ion exchange column
  Half-life 66 hours
Daughter radionuclide
  Technetium-99m
  Eluted from column with saline
  Half life 6 hours
  140keV gamma emission

## Slide 20: Technetium-99m generator

## Slide 21: Radionuclide properties
Thallium-201
Cyclotron produced
79keV X-ray (88%)
135keV + 167keV γ-rays (12%)
Half life 72 hours
Typical effective dose 18mSv
Technetium-99m
Generator produced
140keV γ emission
Half life 6 hours
Typical effective dose 10mSv

## Slide 22: 99mTc perfusion tracers
MIBI
tetrofosmin
furifosmin
NOET
teboroxime
+
+
+

## Slide 23: Physiological properties
Thallium
  Part passive into negative intracellular potential
  Part active via Na+/K+ ATPase dependent pump
  Free exchange with extracellular thallium
  Renal excretion
MIBI
  Passive into negative intracellular potential
  Fixed in mitochondria
  Hepato-biliary excretion
Tetrofosmin
  Passive into negative intracellular potential
  Fixed in cytosol
  Hepato-biliary excretion

## Slide 25: Implications of non-linear uptake
1 Intercept above zero
  Overestimation of reduced perfusion
  Reduced defect contrast
  Overestimation of viability
2 Reduced slope
  Reduced extraction and low counts
  Reduced defect contrast
3 Early plateau
  Underestimation of hyperperfusion
  Reduced defect contrast

## Slide 26: Properties of tracers
 | Thallium | MIBI | Tetrofosmin
Extraction (max) | 0.80 | 0.39 | 0.30
Extraction (5 min) | 0.60 | 0.41 | 0.30
Cell injury reduces uptake | ++++ | ++++ | ++++
Redistribution | yes | minimal | no
Measure of hyperaemia | +++ | ++ | ++
After Leppo JA |  |  | 

## Slide 27: Thallium redistribution

## Slide 28: Patterns of uptake
stress
redistribution
Thallium-201

## Slide 29: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 30: Myocardial perfusion reserve
Uren NG et al. NEJM 1994; 330: 1782-8
35 CAD, 21 controls, adenosine stress, 15O-water PET

## Slide 31: Cardiovascular stress
Exercise
  Dynamic
  Isometric
Other
  Pacing
  Cold pressor
Vasodilators
  Adenosine
  Dipyridamole
  Regadenoson
Inotropes
  Dobutamine

## Slide 32: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 33: Emission tomography
Notes: During SPECT image acquisition for myocardial perfusion imaging, 1 or 2 detectors or heads rotate around the long axis of the patient, acquiring planar images in a step-and-shoot fashion.

## Slide 34: Projection images
Projection images
“raw data”

## Slide 35: Transverse Tomograms
Right
Left
Anterior
Posterior
Cranial
Caudal

## Slide 36: Full study Display

## Slide 37: Triangulation
LAD
LAD
LAD
LAD
RCA
RCA
RCA
LCx
LCx
LCx
LAD
LAD

## Slide 38: Quantification
Polar plot
3D display
Anterior
Inferior
Septum
Lat

## Slide 39: Segmental models
9 segments
17 segments

## Slide 40: ECG gated acquisition
Gated image
function
Summed image
perfusion
ED
ES
ED

## Slide 41: Quantification

## Slide 42: Imaging protocols
Thallium Stress – redistribution
  Stress – redistribution – reinjection
  Stress – reinjection
  Stress – reinjection – 24 hour imaging
  Rest
  Rest – redistribution
Technetium Two day
  One day, stress – rest
  One day, rest – stress
Dual isotope Rest thallium – stress technetium
  Others
Adjuncts Nitrate
  Fatty meal

## Slide 43: Thallium protocol
Stress
Tl 80MBq
Redistribution image
Tl 40MBq
Reinjection image
5 min
4 hr
5 hr
Stress image

## Slide 44: Thallium protocol
Stress
Tl 80MBq
Stress image
Tl 40MBq
Reinjection image
5 min
1 hr

## Slide 45: One day technetium protocols
Stress
Tc 250MBq
Stress image
Tc 750MBq
Rest image
1 hr
5 hr
4 hr
Tc 250MBq
Stress image
Tc 750MBq
Rest image
1 hr
5 hr
Stress
Stress-rest
Rest-stress

## Slide 46: Technetium protocols
 | Advantages | Disadvantages
Two day | no image contamination ECG gating of stress and rest | often impractical
One day stress-rest | high contrast stress images ideal for diagnosis single injection if normal ECG gating of rest images | low count stress images
One day Rest-stress | high contrast rest images ideal for viability | low count rest images ECG gating of stress images only higher radiation if normal

## Slide 47: Dual isotope protocol
Advantages | Disadvantages
Thallium for viability and technetium for ECG gating Shorter for patient | Thallium needs redistribution ± nitrate for viability No less camera time Highest radiation exposure (contravenes ALARA) Normal patients have full procedure Comparison of different tracers Expensive

## Slide 48: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography

## Slide 49: Inducible Perfusion Abnormality
Stress
Rest

## Slide 50: Inducible and Fixed Abnormalities
Stress
Rest
Short Axis Thallium

## Slide 51: Site of Perfusion Defect

## Slide 52: Extent of Perfusion Defect

## Slide 53: Image interpretation
The basal anterior wall shows:
Partial thickness infarction
Mild ischaemia
Moderate ischaemia
Severe ischaemia
Reverse redistribution
Stress
Rest
Score
2
1
0
4
4
4
4
2
4
4

## Slide 54: Radionuclide ventriculography
Labelling of autologous erythrocytes with technetium-99m
ECG gating is used to acquire 16 to 32 frames through the cardiac cycle
Imaging of first-pass of tracer through heart and/or after blood-pool equilibrium
First-pass good for RV function and L  R shunting
Equilibrium good for LV function, systolic and diastolic

## Slide 55: First pass RNV

## Slide 56: Equilibrium RNV
RV
LV
ED
ES
ED

## Slide 57: Quantification

## Slide 58: Principles of Radionuclide Imaging
Properties of gamma rays
The gamma camera
Radiopharmaceuticals
Stress testing (seminar)
Acquiring images
Interpreting images
Radionuclide ventriculography