## Slide 1: BSc in Cardiovascular Science
Bruno Rojas
Department of Nuclear Medicine
Royal Brompton Hospital
Radiation
Protection

## Slide 2: Talk Outline
Origin of Ionising Radiation
  production of Gamma rays
  productions of X-rays
Protection against ionising radiation
  detrimental effects
  dose limits
  risks to foetus
  principles of radiation protection

## Slide 3: Discovery of ‘Radiation’
1895
1896
X-rays
Radioactivity

## Slide 4: THE ORIGIN OF IONISING RADIATION
Radiation is energy that travels through space or matter
Two types important in diagnostic imaging
  electromagnetic
  particulate

## Slide 5: ELECTROMAGNETIC RADIATION
No mass
Unaffected by either electrical or magnetic fields
Has a constant speed in a given medium
Does not require matter for propagation

## Slide 6: ELECTROMAGNETIC RADIATION
Characterised by wavelength (), frequency (), energy per photon (E)
Electromagnetic spectrum:

## Slide 7: ELECTROMAGNETIC RADIATION
EM radiation behaves like waves and/or particles
Wave characteristics
c = 
Particle characteristics
where E is energy of the photon/quanta
h is Planck’s constant
E = h = hc/

## Slide 8: ELECTROMAGNETIC RADIATION
On the EM spectrum, radiation of frequency higher than visible light carries sufficient energy to remove bound electrons from atomic shells
Results in ionised atoms and molecules…
…IONISING RADIATION

## Slide 9: PARTICULATE RADIATION
Protons - in nuclei of all atoms
Electrons - in orbits surrounding atomic nucleus
Beta particles – e- (electrons) emitted by nuclei of radioactive atoms
Positrons – e+, emitted from nuclei
Alpha particles - 2 protons and 2 neutrons

## Slide 10: NUCLEAR STABILITY
Only certain combinations of neutrons and protons in nucleus are stable
Two kinds of instability:
neutron excess
neutron deficiency
Unstable nuclei have excess internal energy
Unstable nuclei are radioactive
Particulate emission to achieve stability

## Slide 11: RADIOACTIVE DECAY - Gamma ray production
Parent nuclide decays to daughter
Daughter nucleus usually in an excited state
Excited state decays to lower (more stable) energy state
EM wave emitted - gamma radiation

## Slide 12: X-RAYS
Can be produced using an x-ray tube:

## Slide 13: X-RAYS
Incident e- fired into close proximity of large electric field of nuclei in target
e- decelerated, resulting in loss of KE
Lost KE released as EM radiation – x-rays
x–rays produced by conversion of electron KE into EM radiation
gamma radiation produced as EM wave emitted from nucleus of atom

## Slide 14
PROTECTION AGAINST IONISING RADIATION

## Slide 15: Early healthcare uses
X-rays
Radioactivity
Imaging
Röntgentherapy/ Radiotherapy
Radium therapy/ Brachytherapy
Quackery

## Slide 16: Early healthcare ‘misuses’
Early 1900’s – no understanding of radiation ‘dose’, limited evidence of harms
X-rays:
  No filtration – large skin dose to patient
  No shielding – staff received large doses
Radioactivity
  Discovered Radium/Radon in spa’s
  Purified Radium for domestic use, huge public demand

## Slide 17: Give them what they want
Esthetic
Domestic
Health

## Slide 18: Radiation Protection in Diagnostic Imaging
Ionising radiation - enough energy to dislodge e-
Human cells impaired - die, genetic effects, cancer
Use of radiation strictly controlled
ICRP consists of specialists in radiation effects
ICRP (60) 1990 recommendations incorporated in legislation
ICRP (103) 2007 recommendations are published, yet to be incorporated

## Slide 19: Detrimental Effects of Radiation
Basically two types -
Deterministic effects: Threshold value; under - no effect; above - severity proportional to dose received
Stochastic effects: No threshold; risk increases with dose received

## Slide 20: Deterministic Effects
Examples:
erythema
Cataracts
radiation sickness
necrosis
Radiation dose
Effect

## Slide 21: Stochastic effects
Examples :
cancer
genetic effects
Radiation dose
Risk
?

## Slide 22: ALARA
“All doses should be kept As Low As Reasonably Achievable, social and economic factors taken into account”

## Slide 23: Radiation Dosimetry
Absorbed Dose, Gray (1 Gy=1 J/kg)
Effective Dose, Sievert (Sv)
adjusted for - radiation type - irradiated organ(s)
to give whole body dose
Effective dose allows comparison of exposures from different means

## Slide 24: Weighting Factors
Radiation Weighting Factors
  photons (all energies) 1
  Electrons/beta (all energies) 1
  protons 5
  alpha particles 20
Tissue Weighting Factors
  skin 0.01
  lung 0.12
  reproductive organs 0.20

## Slide 25: Dose Limits for staff and public
Prevent deterministic effects
Limit (reduce) stochastic effects (mainly cancer) to acceptable levels
Level of acceptability differs for radiation workers and members of the public

## Slide 26: Dose Limits - Factors considered
Perceived acceptable mortality risks
Workers:
  mortality risk of 1/100 is unacceptable
  mortality risk of 1/1 000 perhaps acceptable
Public:
  public hazard with mortality risk of 1/100 000 perhaps acceptable
Age at exposure

## Slide 27: Mortality Risks
Activities carrying a 1 in 10,000 risk of death:
Whole body exposure to 2 mSv ionising radiation
Smoking 150 cigarettes
Travelling 5000 miles by car
Travelling 25,000 miles by passenger aircraft
Effective doses of some typical medical procedures:
Chest x-ray 0.02-0.05 mSv
Nuclear Medicine 99mTc bone scan 3 mSv
Abdominal CT 4 mSv
18F FDG PET scan 10 mSv

## Slide 28: Cancer Risk
Chance for fatal cancer (general)
= 5% per Sv exposure
= 1 in 20 per Sv exposure
= 1 in 20,000 per mSv

## Slide 29: Evidence of risk
Hibakusha of Hiroshima and Nagasaki
Chernobyl liquidators
Uranium Miners

## Slide 30: Annual Dose Limits*
Workers:
Effective dose (whole body) - 20 mSv per year
Equivalent doses lens of eye - 150 mSv per year (soon 20mSv)
1cm2 skin - 500 mSv per year
extremities – 500 mSv per year
Public:
Effective dose (whole body) - 1 mSv per year
Equivalent doses lens of eye - 15 mSv per year
1cm2 skin - 50 mSv per year
extremities – 50 mSv per year
*Taken from The Ionising Radiation Regulations 1999 (and ICRP 2011 Statement on tissue reactions)

## Slide 31: Effective doses from typical examinations
Category | Examination | Effective Dose, mSv
Simple x-ray | Chest | 0.05
Simple x-ray | Skull | 0.15
Simple x-ray | Abdomen or pelvis | 1
Complex x-ray | IVU | 3.5
Complex x-ray | Barium meal | 3
Complex x-ray | Barium enema | 7
CT | Spiral CT abdomen | 4
Nuclear Medicine | Tc-99m bone scan | 3
Nuclear Medicine | Tc-99m MPI cardiac | 10

## Slide 32: Radiation Risk to Foetus
Radiation exposure may cause detrimental effects such as:
  death of foetus
  abnormalities/malformation of limbs and organs
  mental retardation
  cancer and genetic effects
New guidance ‘Protection of Pregnant Patients during Diagnostic Medical Exposures to Ionising Radiation’
  http://www.hpa.org.uk/web/HPAwebFile/HPAweb_C/1238230848746

## Slide 33: Radiation Risk to the Foetus
For typical range of fetal dose given in diagnostic medicine (much less than 100mGy threshold)- no risk of causing fetal death, malformation, growth retardation of impairment of mental development
Main concern- childhood cancer induction (stochastic effect with no threshold)

## Slide 34: Radiation Risk to the Foetus- Cancer Induction
Fetal dose is grouped into bands- to cover the wide range of dose due to equipment variation and the uncertainties in the risk estimates
Baseline risk of childhood cancer is 1 in 500
The excess absolute risk factor for incidence of childhood cancer is ~1 in 10,000 per mGy
Fetal dose of ~25mGy will lead to double the risk of childhood cancer

## Slide 35: Radiation Risk to the Foetus
Exam | Typical fetal dose range (mGy) | Risk of childhood cancer per exam
Xray skull | 0.001-0.01 | <1 in 1,000,000
Xray chest | 0.001-0.01 | <1 in 1,000,000
Xray CT pulmonary angiogram | 0.01-0.1 | 1 in 1,000,000 to 1 in 100,000
Xray abdomen | 0.1-1.0 | 1 in 100,000 to 1 in 10,000
99mTc renal scan (DMSA, MAG3) | 0.1-1.0 | 1 in 100,000 to 1 in 10,000
Xray barium enema | 1.0-10 | 1 in 10,000 to 1 in 1,000
99mTc bone scan | 1.0-10 | 1 in 10,000 to 1 in 1,000
Xray CT pelvis | 10-50 | 1 in 1,000 to 1 in 200
18F PET/CT whole body | 10-50 | 1 in 1,000 to 1 in 200

## Slide 36: Advice regarding Termination of Pregnancy – Diagnostic Procedures
For majority of diagnostic exposures to a pregnant woman (fetal dose up to 1mGy) associated risks in childhood are deemed acceptable when compared to natural risk
For typical exposures (fetal dose 1-50 mGy) care should be taken in justification process and these exams should be avoided if without causing detrimental effects on health
Termination of pregnancy unlikely to be justified even following higher dose procedures (e.g. pelvic CT)

## Slide 37: Normal Pregnancy Risks
  spontaneous abortion 15%
  important abnormalities 3%
  significant mental retardation 0.5%
  genetic illness 8-10%
  cancer 0.1%

## Slide 38: Principles of Radiation Protection
TIME
DISTANCE
SHIELDING

## Slide 39: Principles of Radiation Protection
Time
Exposure time is directly proportional to effective dose
All work resulting in radiation exposure must be completed as quickly as possible

## Slide 40: Principles of Radiation Protection
Distance – the exposure rate, X, of radiation is inversely proportional to the square of the distance from its origin
Always keep as far as possible from radiation

## Slide 41: Principles of Radiation Protection
1m
2m
dose
¼ dose

## Slide 42: Principles of Radiation Protection
Shielding
To protect from radiation, when one must be close to the source, a shield of appropriate material may be used. The thickness, d, can be calculated from
Xd = X0e-md
where X0 is the exposure rate at origin, Xd the exposure rate desired and m is the attenuation coefficient of the shielding material
Always use shielding when advised

## Slide 43: Summary
There are risks associated with radiation exposure
  Deterministic effects (burns etc)
  Stochastic effects (cancer)
Staff and public doses must be kept below the dose limits and ALARP
Patient doses must be clinically justified