## Slide 1: Laboratory tests of coagulation
Professor Mike Laffan
Department of Haematology
Hammersmith Hospital

## Slide 2: LEARNING OBJECTIVES
Understand the ways in which haemostatic mechanism fail
Understand the principles of different laboratory tests in coagulation
Understand the limitations associated with laboratory tests in coagulation
Be aware of pre-analytical variables
Understand the principles of automation

## Slide 3: Why do people bleed? -Defects of procoagulant function
Too little protein (quantitative)
  Usually inherited specific assays
  Excess consumption global pattern
  Liver failure global pattern
  Drugs, antibody, hormonal specific assays
Defective function (qualitative)
  Usually inherited specific assays
Inhibited function
  Antibody present specific assays
  Drugs

## Slide 4
Haemostatic Plug Formation: An Overview
Vessel constriction
Formation of an unstable platelet plug
-platelet adhesion
-platelet aggregation
Stabilisation of the plug with fibrin
-blood coagulation
Dissolution of clot and vessel repair
-fibrinolysis
Response to injury

## Slide 5: Tests of the coagulation system

## Slide 6: Coagulation: ‘Screening tests’
Prothrombin time (PT)
Activated partial thromboplastin time (APTT)
  Kaolin cephalin clotting time (KCCT)
  Partial thromboplastin time with Kaolin (PTTK)
Thrombin time (TT)
Fibrinogen assay
(Platelet count)

## Slide 7
Tissue thromboplastin
Surface Contact
Blood or plasma
‘Clot’

## Slide 8
Fibrinogen
Fibrin
Tissue thromboplastin
Surface Contact
Thrombin

## Slide 9
IX
Fibrinogen
Fibrin
Thrombin
Tissue thromboplastin
PK
HMWK
XI
XII
VIIa
VIII
X
V
Surface Contact
PT
APTT

## Slide 10: Classical model of coagulation
Two systems
  Intrinsic – contact activated
  Extrinsic – tissue extract activated
Systems give inconsistent results
  Tissue factor thought to initiate in vivo
  PT normal in haemophilia
  FXII gives very long APTT but no bleeding

## Slide 11: Resolution of two systems
TF-VIIa activates both pathways:
  Factor X - extrinsic pathway
    Extrinsic path turned off by TFPI (in vivo)
  Factor IX – intrinsic pathway
    Intrinsic pathway then responsible for thrombin burst

## Slide 12
?
IX
Fibrinogen
Fibrin
Thrombin
Tissue factor
PK
HMWK
XI
XII
VIIa
VIII
X
V
Surface Contact
Tissue factor is the physiological initiator of coagulation

## Slide 13: Factor XI?
Final problem was FXI deficiency which is associated with a mild bleeding disorder.
Resolved by demonstration that thrombin can activate FXI directly on platelet surface
  Bind to GPIb-IX-V complex
Additional FXI dependent thrombin generation required for TAFI activation

## Slide 14: Routine coagulation testing
Practical but unphysiological

## Slide 15
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT
APTT
TT
IIa

## Slide 16: Coagulation: ‘Screening tests’
Prothrombin time (PT)
  Trigger: Thromboplastin (Tissue factor)
  Requires factors: VII, X, V, II, Fibrinogen
  Calcium

## Slide 17
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT 22 (9.6-11.6)
APTT 28 (26-32)
TT 16 (15-19)
PROLONGED PT

## Slide 18
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PROLONGED PT
FVII deficiency

## Slide 19
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT
APTT
TT
IIa

## Slide 20: Coagulation: ‘Screening tests’
Activated partial thromboplastin time (APTT)
  Trigger: contact activator:
    Kaolin, silica, elagic acid, glass
  Requires factors XII, PK, HMWK, XI, VIII, IX, X, V, II, Fibrinogen.
  Calcium

## Slide 21
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT 10.6 (9.6-11.6)
APTT 65 (26-32)
TT 16 (15-19)
PROLONGED APTT

## Slide 22
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
Deficiency of
Contact factor
(XII, PK, HMWK)
FXI, FIX, FVIII
PROLONGED APTT

## Slide 23
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT
APTT
TT
IIa

## Slide 24: Coagulation: ‘Screening tests’
Thrombin time (TT)
  Requires: Fibrinogen
  (absence of inhibitors such as heparin)

## Slide 25
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT 10.5 (9.6-11.6)
APTT 28 (26-32)
TT 33 (15-19)
PROLONGED TT

## Slide 26
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
Inhibitor of thrombin
(eg heparin)
Inhibitor of polymerisation
Abnormal fibrinogen
PROLONGED TT

## Slide 27
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT 19.3 (9.6-11.6)
APTT 45 (26-32)
TT 16 (15-19)
PROLONGED APTT AND PT

## Slide 28
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
Deficiency
FV, FX, Prothrombin
OR
Multiple deficiencies
PROLONGED APTT AND PT

## Slide 29
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT 18.5 (9.6-11.6)
APTT 45 (26-32)
TT 27 (15-19)
ALL TESTS PROLONGED

## Slide 30
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
Fibrinogen deficiency
Abnormal fibrinogen
Multiple deficiencies
Combination (DIC)
ALL TESTS PROLONGED

## Slide 31: Why coagulation screens?
Detect a bleeding tendency
Detect a cause for bleeding
Detect a systemic disease
Detect a thrombotic disorder
‘reassurance’

## Slide 32
In fact they are reliable for none of these things
Coagulation screens are usually performed to detect a defect in haemostasis
- have limited sensitivity & specificity
Coagulation screens test a very limited portion of haemostasis

## Slide 33
0
concentration / iu/ml
0
60
120
240
300
420
180
360
0.2
0.4
0.6
0.8
0
0.2
0.4
0.6
0.8
incubation/secs
0
60
120
240
300
420
180
360
Sensitivity of the APTT
FVIII
FXII
FXII
FVIII

## Slide 34: Actin FS sensitivity factor deficiency
Lawrie 1998

## Slide 35: APTT sensitivity to coagulation factor deficiency
Sensitive to contact factor deficiency (irrelevant)
  False positives
What is appropriate level of sensitivity for VIII,IX, XI ?
  False positives and false negatives

## Slide 36
Bleeding disorders not detected by
routine clotting tests
Mild factor deficiencies
von Willebrand disease
Factor XIII deficiency (cross linking)
Platelet disorders
Excessive fibrinolysis
Vessel wall disorders
Metabolic disorders (e.g. uraemia)
(Thrombotic disorders)

## Slide 37: Screening tests for other elements of haemostasis
Platelet count
Bleeding time
PFA 100 analyser
Euglobulin clot lysis time
Global tests: TEG, ETP

## Slide 38: Coagulation tests and factor deficiencies

## Slide 39
Coagulation testing
Prolonged global clotting tests (screening tests)
Correction (mixing) tests
Specific factor assays
Inhibitor tests and assays
+
_

## Slide 40
Assays of coagulation factors
1. Antigenic assays (usually ELISA)
not necessarily relevant
precise
not prone to interference

## Slide 41: IMMUNOLOGICAL ANTIGEN ASSAYS
Immunological antigen assays give an indication of how much protein is present but not activity
a Enzyme immunoassays (ELISA)
b Immunoturbidimetric assays

## Slide 42
ELISA assay
Capture antibody bound to plate
APAAP conjugated
detection antibody
Test molecule

## Slide 43
LIA: immunoturbidimetric assay
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Latex particles coated with anti-VWF
VWF

## Slide 44
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Latex particles coated with anti-VWF
VWF
Agglutination measured turbidimetrically
LIA: immunoturbidimetric assay

## Slide 45
Y
Y
Y
Y
Y
Light detector
VWF
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Light source
LIA: immunoturbidimetric assay

## Slide 46: Laurell Rocket

## Slide 47
Enzyme Linked ImmunoSorbent Assay
ELISA assay
Capture antibody bound to plate
MPO conjugated
detection antibody
Test molecule
Notes: This is a sandwich type assay

## Slide 48: ELISA

## Slide 49: Quantification
Use a series of dilutions made from the reference preparation
Create a ‘standard curve’
Modify as necessary to obtain a straight line with useful span and spread of values
Quantify your sample by comparison with the ‘standard curve’

## Slide 50: Limits of detection

## Slide 51: Quantitation of test sample

## Slide 52: ELISA
Need one or more specific antibodies
  Mono- or poly-clonal Abs are both used
One antibody coupled to enzyme or a second enzyme-linked antibody can be used.
Need a calibrant of known concentration
Usually performed in a 96 well plate
Problems
  Background or non-specific binding
  Limit of sensitivity
  Relatively time consuming

## Slide 53: Immunoturbidimetric assay
Antibody is bound to latex beads
Presence of antigen cross links binds
Agglutination causes increase in turbidity
Turbidity measured by light transmission
Need a calibrant of known concentration
Accurate, precise, easily automated
Problems
  Cross linking by Rheumatoid factor or autoantibody

## Slide 54
LIA
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Latex particles coated with anti-VWF
VWF

## Slide 55
LIA
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Latex particles coated with anti-VWF
VWF
Agglutination measured turbidimetrically

## Slide 56
LIA
Y
Y
Y
Y
Y
Light detector
VWF
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Y
Light source

## Slide 57: Coagulation factor assays
Antigenic assays
Bioassays
  Measure biological activity of the analyte
  Prone to interference by other factors
  Poor accuracy and precision (CV)
  Based on routine screening tests (Clot end point)

## Slide 58
IX
II
Fibrinogen
Fibrin
PK
HMWK
XI
XII
VIIa
TF
VIII
X
V
CONTACT
PT
APTT
TT
IIa

## Slide 59: Coagulation factor bioassay
APTT based assay for VIII, IX, XI, XII
PT based assay for VII, V, X, II
RVVT can also be used

## Slide 60: Coagulation factor bioassay
Factor deficient plasma
Calibrant/reference plasma of known potency
Test plasma of unknown potency
APTT or PT reagent
Phospholipid and Calcium
Internal controls

## Slide 61
Parallel line bio-assay
The one-stage clotting assay
  Dilutions of test plasma or reference standard are added to factor deficient plasma and the clotting times recorded (using PT or APTT)
Principle
  The test plasma behaves as a simple dilution of the standard
  Dilutions of test and standard can be plotted as parallel lines
Value for test is read off from standard curve

## Slide 62
Reference
Test

## Slide 63: Quantitation
Test
*55%
*55% of the standard
If standard is 0.9u/ml then 0.9 x .55 = 0.49 iu/ml

## Slide 64: SNAKE VENOMS
Bothrops jacaraca (fibrinogen to fibrin)
Bothrops atrox (Reptilase, thrombin-like activity)
Oxyuranus scutellatus (Taipan venom, FII assay)
Vipera russeli (Russell’s viper, FX activation)
Agkistrodon contortrix (Protein C activation)
Can be used as trigger for functional assays

## Slide 65: Chromogenic Assay General Principle
Activator
Zymogen
Enzyme
Enzyme
Peptide
PNA
Peptide
PNA
Yellow colour develops
(Substrate)
+
Colourless
Proportional to enzyme concentration

## Slide 66: CHROMOGENIC ACTIVITY ASSAYS
A chromogenic substrate is cleaved by the enzyme of interest and colour generation measured
Chromogenic activity assays are an alternative to clotting activity assays and may be more reproducible but are not always physiological.
Specific substrates are available for:
a Kallikrein
b Factor Xa
c Thrombin
d Activated Protein C
e Plasmin
f Urokinase.

## Slide 67: Tests of primary haemostasis

## Slide 68: Primary haemostasis
Vessel wall
Von Willebrand factor
Platelets
(some contribution from other adhesive molecules: fibrinogen, vitronectin, fibronectin)

## Slide 69: The bleeding time
Can be standardised using a template
Now generally obsolete
  Poor sensitivity
  Poor specificity
  Poor reproducibility
  Poor predictive value
Possibly of use in suspected collagen disorder
Replaced by laboratory analysers eg: PFA 100

## Slide 71: PFA100
Sensitive to:
  Platelet number
  Platelet function
  VWF adhesive function
  Haematocrit
Insensitive to
  Thrombin generation
  Mild platelet function defects
  Clopidogrel

## Slide 72: Platelet function testing
Platelet number
  FBC
Platelet aggregation
  Measure aggregation in response to standard agonists.
Global tests
  Bleeding time
  PFA
Platelet granule contents
  ATP:ADP ratio

## Slide 73: Preparation of PRP and PPP

## Slide 74
Platelet aggregation testing in platelet rich plasma
AGONIST
time
Light transmission
Notes: PRP Prepared from citrated blood (200g and 1500g)
Do not adjust platelet count of PRP (unless >600) as this may cause artefactual inhibition. Needs to be >150
37 oc stirred by magnetic stirrer. Watch for lipaemic or icteric samples.
Calibrate curve with PRP and PPP

## Slide 75: Platelet aggregation: agonists
ADP 1, 2.5, and 5 (10) M
Epinephrine 10M
Collagen 1.25 and 4 gmL-1
Ristocetin 0.5 and 1.5 mgmL-1
Arachidonic acid 500 gmL-1

## Slide 76
Platelet aggregation with ADP

## Slide 77: Other factor assays
Most factors in anticoagulant and fibrinolytic pathways can be assayed.
Assays conform to previous types:
  Antigenic
  Functional clot based
  Functional chromogenic substrate

## Slide 78: PRE-ANALYTICAL VARIABLES How to ensure meaningful results
1 Effects of stress and exercise
Factor VIII & VWF rise with exercise
2 Blood sample collection
    a Venepuncture Technique
    b Blood sample containers
    c Choice of anticoagulant (Citrate)
    d Special inhibitors
    d Timing of collection
    Fibrinolysis has diurnal variation

## Slide 79: PRE-ANALYTICAL VARIABLES
3 Sample transport to the laboratory
The in vivo half-life of FVIII is 10 hours
4 Centrifugation (Speed, temperature and time)
5 Storage of plasma (Temperature and time)

## Slide 80: Normal centrifuged citrate sample
Platelet poor plasma
Buffy coat (plts and wbc)
Packed red cells

## Slide 81: UNACCEPTABLE SAMPLES
1 Incorrect proportion of blood to anticoagulant
2 Haemolysed samples
3 Clotted or activated samples

## Slide 82: Underfilled, Haemolysed and a good quality citrate sample

## Slide 83: AUTOMATION IN COAGULATION
Increase the throughput of samples
Increase precision
Relieve the strain of manual clotting
Types of End-Point detection
1 Electro-mechanical devices - impedance
2 Light transmission and light scatter
Clotting assays
Chromogenic assays
Immunological assays

## Slide 84: AUTOMATION IN COAGULATION
Pros
  Very high throughput
  Multiple assays on single samples
  Good reproducibility (precision)
Cons
  Susceptible to end point errrors (lipaemia, jaundice, low fibrinogen)
  Introduce artefacts

## Slide 86: Endpoint detection
Endpoint
Absolute level
Change from baseline
Rate of change