## Slide 1: An introduction to biomechanics
a.bull@imperial.ac.uk
www.bg.imperial.ac.uk/staff/abull
Dr Dominic Southgate
Sports Bioengineering Teaching and Research Fellow
Department of Bioengineering
January 2013

## Slide 2: Lecture content
Part 1 – General Mechanics
Part 2 – Mechanics in the Body

## Slide 3: Learning Outcomes
Part 1 – General Mechanics:
• Define loading, stress and strain
• Describe how materials can be tested for their mechanical properties

## Slide 4: Learning Outcomes
Part 2 – Mechanics in the Body:
• Explain how the structures in the body are related to function
• Describe the levels of biomechanical assessment including muscle and joint motion that can be applied to assess human motion and function
• Estimate joint loading

## Slide 5: Learning Outcomes
Part 2 – Mechanics in the Body:
• Apply a knowledge of mechanics to the design of an implant for use in gastrointestinal, orthopaedic, vascular and other specialist surgeries
• Illustrate how a knowledge of mechanics can explain features of disease presentation and progression in the field of musculoskeletal or vascular medicine

## Slide 6: Learning Outcomes
Both parts may also help you:
• Recognise the limitations of tools to assess performance
• Manage and interpret data within the context of its acquisition
• Judge the quality of research outputs

## Slide 7: What is Biomechanics?
"The study of forces acting on and generated within the body and of the effects of these forces on the tissues, fluids or materials used for diagnosis, treatment or research purposes."

## Slide 8: Applications
Research e.g.
Osteoarthritis Centre

## Slide 9: Applications
Research e.g. shoulder

## Slide 10: Applications
Research e.g. sports medicine

## Slide 11: Part 1 – General Mechanics
Basic Concepts Combining&Calculating Stress&Strain

## Slide 12: Part 1 – General Mechanics
Forces and Moments
Equilibrium
Free Body Diagrams
Bending, Torsion, Shear
Stress and Strain
Young’s Modulus
Basic Concepts Combining&Calculating Stress&Strain

## Slide 13: Sources of Force
External
Internal
Friction
Acceleration
Weight (Weight = mass × g ; g is a type of acceleration)
Basic Concepts Combining&Calculating Stress&Strain

## Slide 14: Force
Basic Concepts Combining&Calculating Stress&Strain
…is a vector
…is measured in Newtons (N)

## Slide 15: Combining Forces
“Resultant”
=
Basic Concepts Combining&Calculating Stress&Strain

## Slide 16: Polygon of forces
=
Basic Concepts Combining&Calculating Stress&Strain

## Slide 17: Combining Forces
“Components”
Fx
Fy
Basic Concepts Combining&Calculating Stress&Strain

## Slide 18: Resolving Forces
Summation: Σ
ΣFx, ΣFy
In equilibrium:
ΣFx = 0
ΣFy = 0
Basic Concepts Combining&Calculating Stress&Strain

## Slide 19: Equilibrium
Basic Concepts Combining&Calculating Stress&Strain
Maximum frictional force = µR
R
µ = coefficient of friction
R = reaction force

## Slide 20: Equilibrium
Basic Concepts Combining&Calculating Stress&Strain
F = m x a
a = F / m
F = resultant force
m = mass
a = acceleration

## Slide 21: Moments
Moment = F × d
F
d
“Moment of a force”
Levers
Measured in Nm
Basic Concepts Combining&Calculating Stress&Strain

## Slide 22: Moments
Moment = M
M
Direct moments
In equilibrium:
ΣM = 0
Basic Concepts Combining&Calculating Stress&Strain

## Slide 23: Free Body Diagrams
A way of calculating unknown forces and moments
Example
Basic Concepts Combining&Calculating Stress&Strain

## Slide 24: Free Body Diagrams
Basic Concepts Combining&Calculating Stress&Strain

## Slide 25: Free Body Diagrams
Basic Concepts Combining&Calculating Stress&Strain
1 unit
10 units
F
R
W

## Slide 26: Free Body Diagrams
Resolve Forces:
ΣFy = 0
F – W – R = 0
Resolve Moments:
ΣMJoint = 0
(F x 1unit) – (W x 10units) = 0
F = W x (10/1) R = …
Basic Concepts Combining&Calculating Stress&Strain

## Slide 27: Modes of loading
Axial
Basic Concepts Combining&Calculating Stress&Strain
Tie (tension)
Strut (compression)

## Slide 28: Examples – Tension/Compression
Ligaments
Tendons
Bone
Articular cartilage
Basic Concepts Combining&Calculating Stress&Strain

## Slide 29: Modes of loading
Shear
Basic Concepts Combining&Calculating Stress&Strain

## Slide 30: Examples – Shear
Tendons
Bone
Articular cartilage
Basic Concepts Combining&Calculating Stress&Strain

## Slide 31: Modes of Loading
Bending
Basic Concepts Combining&Calculating Stress&Strain
Beam

## Slide 32: Examples - Bending
Fracture plates
Fracture fixation pins
Bones
Basic Concepts Combining&Calculating Stress&Strain

## Slide 33: Modes of Loading
Torsion
Basic Concepts Combining&Calculating Stress&Strain
Shaft/axle

## Slide 34: Examples - Torsion
Fracture plates
Bones
Basic Concepts Combining&Calculating Stress&Strain

## Slide 35: Bending
+s
y
-s
Compression
Tension
Basic Concepts Combining&Calculating Stress&Strain

## Slide 36: Combined Loading
+s
y
-s
+s
y
-s
+s
y
-s
+
=
Compression
Tension
Basic Concepts Combining&Calculating Stress&Strain

## Slide 37: Materials Testing
Basic Concepts Combining&Calculating Stress&Strain

## Slide 38: Materials Testing
Measure force
Measure extension
Basic Concepts Combining&Calculating Stress&Strain

## Slide 39: Materials Testing
Elastic deformation
Plastic deformation
Basic Concepts Combining&Calculating Stress&Strain

## Slide 40: Distribution of load/force
F
F
F
F
Basic Concepts Combining&Calculating Stress&Strain

## Slide 41: Stress
Stress (normalised Force)
Pressure (acting equally in all directions)
Stress or Pressure = Force/Area
Area
Basic Concepts Combining&Calculating Stress&Strain

## Slide 42: Normalisation of extension
F
F
F
F
Basic Concepts Combining&Calculating Stress&Strain

## Slide 43: Strain
Normalised Extension
Strain = Extension/Original Length
F
F
L
x
Basic Concepts Combining&Calculating Stress&Strain

## Slide 44: Stiffness
Extension per unit force
“Young’s Modulus”
  Normalised stiffness
= Stress/Strain
Basic Concepts Combining&Calculating Stress&Strain

## Slide 45: Normalising Stiffness
σ = F / A
ε = ΔL / L
Basic Concepts Combining&Calculating Stress&Strain

## Slide 46: Young’s Modulus
Units: Pa (N/m2) x109 or GPa
Steel
Aluminium
Bone
Ligaments
Cartilage
Basic Concepts Combining&Calculating Stress&Strain

## Slide 47: Summary
Forces and Moments
Equilibrium
Free Body Diagrams
Bending, Torsion, Shear
Stress and Strain
Young’s Modulus

## Slide 48: Part 2 – Mechanics in the Body
Intersegmental Finite Element Cadaveric Testing

## Slide 49: Part 2 – Mechanics in the Body
Cadaveric Testing
Intersegmental models
Finite Element models
Intersegmental Finite Element Cadaveric Testing

## Slide 50: Cadaveric Testing
Intersegmental Finite Element Cadaveric Testing
Uses
Establishing material properties
Investigating joint laxity and restraints
Simulating pathology and surgical intervention

## Slide 51: Ligament/Tendon
‘Viscoelastic’
Load-extension response is time dependent
Intersegmental Finite Element Cadaveric Testing

## Slide 52: Ligament/Tendon
Toe region
Uncrimping of fibres
Gradual fibre recruitment
Linear region
Straight fibres
Full fibre recruitment
Multiple failure region
Fibres fail sequentially
Rupture
Intersegmental Finite Element Cadaveric Testing

## Slide 53: Cadaveric Testing
Intersegmental Finite Element Cadaveric Testing
Long head of biceps tendon
Tensile test to failure
Example studies:
Alexander et al., 2009, Shoulder and Elbow.

## Slide 54: Cadaveric Testing
Intersegmental Finite Element Cadaveric Testing

## Slide 55: Simulating Clinical Motions
Intersegmental Finite Element Cadaveric Testing
Anterior drawer test
Example studies:
Southgate et al., 2009, J Biomech.
Alexander et al., 2013, J Shoulder Elbow Surg

## Slide 56: Cadaveric Testing
Intersegmental Finite Element Cadaveric Testing
Southgate et al., Arthroscopy (In Review).
Humeral Avulsion of the Glenohumeral Ligament (HAGL) lesions

## Slide 57: Cadaveric Testing
Intersegmental Finite Element Cadaveric Testing
Chart: Normalised Data
| 5 | 10 | 15 | 20 | 25 | 30
Intact | 2.2397 | 9.7812 | 21.2401 | 39.5825 | 69.5846 | 100
Medium HAGL | 0.42921 | 7.4225 | 23.4528 | 46.0305 | 71.4319 | 110.077
Large HAGL | 0.32531 | 10.9846 | 31.491 | 57.6715 | 84.717 | 120.6961
Juxtachondral Repair | 1.4297 | 11.6286 | 24.4082 | 51.1336 | 80.2134 | 116.0864
Anatomical Repair | 1.1379 | 10.008 | 22.1931 | 38.1145 | 66.1341 | 101.1588

## Slide 58: Cadaveric Testing Limitations
Intersegmental Finite Element Cadaveric Testing
Specimens may have existing pathology
Variability in anatomy between specimens
Material properties can change if not kept in physiological environment
Reproducing in-vivo loading is challenging
Isolating structures can also be difficult
Often single experiment per specimen only
…Expensive!

## Slide 59: Cadaveric Testing Summary
Intersegmental Finite Element Cadaveric Testing
Useful for investigating material properties, whole joint motion and effects of surgery
Need to be aware of complex loading environments
Limitations of cadaveric testing may prevent direct translation into clinical practice

## Slide 60: Types of Biomechanical Model
Intersegmental models
Each bone/muscle/ligament treated as a single element
Calculates joint reaction forces and predicts muscle tension
Finite Element models
Each bone/muscle/ligament divided into many small elements
Calculates distribution of stress/strain within the tissues
Intersegmental Finite Element Cadaveric Testing

## Slide 61: Intersegmental Modelling
Forward Dynamics How forces cause movements. Estimate the movement resulting from forces and moments
Kinematics Movements (position, velocity, acceleration, joint angles)
Kinetics
Forces during movements (joint torque, GRF)
Inverse Dynamics How movements require forces. Estimate the forces that cause the motions we measure
Intersegmental Finite Element Cadaveric Testing

## Slide 62: Intersegmental Modelling
1 unit
10 units
F
R
W
Intersegmental Finite Element Cadaveric Testing

## Slide 63: Intersegmental Moments
M = 50(0.3cos(q-90))
50 N
0.3m
q
Intersegmental Finite Element Cadaveric Testing

## Slide 64: Intersegmental Modelling
Intersegmental Finite Element Cadaveric Testing

## Slide 65: Intersegmental Modelling
Motion Capture
Kinematic analysis
Intersegmental Finite Element Cadaveric Testing

## Slide 66: Intersegmental Modelling
Motion Capture
Kinematic/kinetic analysis can be used directly…
Example studies:
Duffell et al., Gait and Posture (In Review).
Intersegmental Finite Element Cadaveric Testing

## Slide 67: Intersegmental Modelling
Inverse Dynamics
Joint force and torque calculation
Intersegmental Finite Element Cadaveric Testing

## Slide 68: Intersegmental Modelling
Anatomical geometry
Segmentation
MRI/CT etc.
Example studies:
Klein Horsman et al., 2007, Clin Biomech.
Intersegmental Finite Element Cadaveric Testing

## Slide 69: Intersegmental Modelling
Optimisation Algorithms
‘Cost function’ to minimise muscle stress
Written (coded) in Matlab/C++
Newcastle Shoulder Model
Intersegmental Finite Element Cadaveric Testing

## Slide 70: Intersegmental Modelling
Output Muscle Forces
Intersegmental Finite Element Cadaveric Testing
Chart: Glenohumeral Muscle Forces
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150
SS | 8.9536 | 16.021 | 31.552 | 46.285 | 61.024 | 75.808 | 89.921 | 102.16 | 91.381 | 100.87 | 110.33 | 118.24 | 125.34 | 130.85 | 135.89 | 138.99 | 137.7 | 129.8 | 120.08 | 111.63 | 101.99 | 90.979 | 78.91 | 63.945 | 44.686 | 24.066 | 3.6668e-19 | 3.5515e-20 | -9.6462e-20 | 1.0748e-20 | 1.3172e-19
IS1 | 1.9483 | 1.9796 | 2.0102 | 3.2235 | 4.5444 | 6.2907 | 8.0992 | 9.9382 | 9.3737 | 10.938 | 12.6 | 14.433 | 16.118 | 17.611 | 19.004 | 20.31 | 21.324 | 21.18 | 20.712 | 20.159 | 19.252 | 18.097 | 17.158 | 15.886 | 13.78 | 11.063 | 9.187 | 4.7164 | 0.52065 | -1.0138e-19 | 3.593e-19
IS2 | 1.7177 | 0.41613 | 4.6135e-20 | -2.6288e-20 | -2.0985e-20 | -1.5936e-20 | 1.0333 | 3.4637 | 3.8429 | 6.6206 | 9.3554 | 12.472 | 15.821 | 18.785 | 21.792 | 24.596 | 26.985 | 27.878 | 28.099 | 28.447 | 28.42 | 28.079 | 28.373 | 28.164 | 26.658 | 23.789 | 23.702 | 18.057 | 9.7523 | 1.5078e-19 | -1.5553e-19
IS3 | -8.4284e-20 | -4.5979e-19 | 3.2118e-20 | -2.886e-20 | 3.5925e-20 | -2.3426e-20 | 5.6643e-20 | -5.1589e-20 | 1.3198e-21 | -1.1106e-19 | 8.3938e-20 | 1.5613e-20 | 0.1429 | 4.6625 | 9.4086 | 14.981 | 19.724 | 22.72 | 25.81 | 28.569 | 31.472 | 34.379 | 38.213 | 41.893 | 43.735 | 43.168 | 48.038 | 43.34 | 31.713 | 27.821 | 12.402
SBS1 | 2.2669 | 1.5804 | 4.0764e-20 | 5.1094e-20 | -2.7409e-20 | 0.82156 | 2.5857 | 5.0481 | 4.1633 | 8.063 | 10.898 | 13.395 | 15.525 | 17.804 | 20.033 | 21.482 | 20.155 | 16.105 | 12.058 | 10.794 | 8.8845 | 7.1062 | 3.9426 | 0.0026847 | 2.7075e-20 | 1.5881e-19 | -3.1145e-19 | -3.9542e-20 | -1.9671e-19 | -1.7331e-20 | 1.2687e-19
SBS2 | 0.81867 | 1.6224 | 2.408 | 3.8076 | 5.6132 | 7.1924 | 9.3198 | 11.567 | 12.292 | 14.32 | 16.567 | 19.076 | 21.715 | 24.959 | 28.319 | 31.402 | 33.983 | 35.589 | 36.736 | 38.716 | 40.195 | 41.358 | 42.901 | 43.217 | 41.361 | 40.512 | 37.306 | 29.15 | 25.567 | 18.945 | 3.948
SBS3 | 0.30201 | 2.8261 | 7.5887 | 10.864 | 14.291 | 17.626 | 21.7 | 25.885 | 28.57 | 31.163 | 35.292 | 40.101 | 45.383 | 52.466 | 59.602 | 66.743 | 74.163 | 81.286 | 87.01 | 92.396 | 97.653 | 101.36 | 107.02 | 110.08 | 108.08 | 109.25 | 105.03 | 87.326 | 87.363 | 89.858 | 120.76
T.min | 1.1179e-19 | 1.0116e-19 | -3.0678e-20 | -1.0664e-20 | 1.6913e-20 | -2.2623e-19 | -1.6084e-19 | 3.906e-21 | -4.0726e-20 | -2.354e-20 | -1.3401e-19 | 1.4532e-20 | -2.651e-19 | 5.059e-20 | 5.0477e-20 | -1.2758e-19 | -1.4325e-19 | 1.7383e-18 | 2.9647e-19 | 2.0163e-19 | 9.286e-22 | 5.4631e-20 | 3.8811e-20 | -2.9998e-19 | 3.9456e-20 | -4.0289e-20 | 2.4673e-19 | 1.6376e-19 | 8.3682e-20 | 3.4088e-19 | -6.8353e-20
T.maj | -1.4527e-19 | 2.5091e-19 | -3.0274e-20 | -3.6857e-21 | -2.1999e-21 | 8.8183e-20 | 2.4672e-20 | 2.0674e-19 | -6.5409e-20 | 1.2669e-19 | -3.5333e-20 | -4.7329e-20 | -7.9155e-20 | -1.1083e-20 | -1.2544e-19 | 1.053e-19 | 1.4652e-19 | -1.079e-19 | -2.9985e-19 | -9.722e-20 | -6.9089e-20 | -4.9811e-22 | -1.9408e-19 | -3.0317e-20 | -7.2282e-20 | -3.4642e-20 | -2.4203e-19 | -1.4787e-19 | -1.0368e-19 | 3.7309e-20 | 3.2804e-20
CB1 | 2.2343e-20 | 3.0694e-19 | 1.2713e-20 | -2.4787e-20 | 1.9709e-21 | 6.91e-20 | -1.5819e-20 | 1.3156e-19 | 9.5627e-20 | -3.0449e-20 | 3.8382e-19 | 5.6799e-20 | 2.541e-19 | 5.9933e-20 | 4.0656e-20 | -3.3844e-20 | 3.2695e-19 | 9.6542e-19 | 1.3034e-19 | 0.46889 | 2.3177 | 4.2721 | 6.297 | 8.4116 | 10.032 | 10.913 | 12.941 | 13.015 | 10.418 | 12.493 | 19.199
CB2 | -4.5546e-20 | -2.1037e-20 | 4.3729e-20 | -1.0819e-20 | 2.1656e-20 | -1.5775e-20 | 4.9131e-20 | 5.6954e-20 | 2.2531e-19 | 4.8058e-20 | 5.4343e-20 | -6.8842e-20 | -1.5574e-19 | -4.622e-20 | -8.7321e-20 | -1.3655e-20 | 3.01e-20 | 4.108e-19 | 1.3079e-20 | 0.77889 | 2.7254 | 4.7692 | 6.9178 | 9.1507 | 10.847 | 11.813 | 13.97 | 14.01 | 11.373 | 13.732 | 21.689
Bic.s | 1.269 | 3.3264e-19 | 1.1508e-20 | -3.5855e-20 | -6.5436e-20 | 3.3367e-21 | -1.7073e-20 | -4.3494e-22 | 6.7629e-20 | -2.6611e-19 | 1.7098e-19 | -8.4074e-20 | -1.8607e-19 | 4.3377e-19 | 1.6218e-19 | -1.9222e-19 | 1.4162e-19 | -3.9915e-19 | -5.3456e-19 | 3.4787e-19 | -5.3327e-20 | 1.6601e-19 | 5.783e-20 | 4.3313e-19 | -7.9195e-20 | 8.412e-20 | 8.0299e-20 | -2.6229e-19 | -3.4622e-19 | 3.1598e-19 | -4.538e-19

## Slide 71: Intersegmental Modelling
Uses
Analysing joint motions
  Diagnosing abnormal patterns
Estimating muscle and joint forces
  Improving implant design etc.
Effects on muscle moment arms
  Changes following surgery
Intersegmental Finite Element Cadaveric Testing

## Slide 72: Intersegmental Modelling
Example studies:
...sensitivity to lower limb kinematics
  Southgate et al., 2012, Proc Inst Mech Eng [H]
...patellofemoral forces during weightlifting and vertical jumping
  Cleather & Bull, 2010, Proc Inst Mech Eng [H]
...biomechanics of reverse shoulder replacement
  Kontaxis and Johnson, 2009, Clin Biomech.
Intersegmental Finite Element Cadaveric Testing

## Slide 73: Finite Element Modelling
Anatomical geometry
Segmentation
MRI/CT etc.
Intersegmental Finite Element Cadaveric Testing

## Slide 74: Finite Element Modelling
Mesh Generation
Element type
No. of elements
Example studies:
Weiss et al., 2005, Med Eng Phys.
Inferior Glenohumeral Ligament Model – Weiss Group
Intersegmental Finite Element Cadaveric Testing

## Slide 75: Finite Element Modelling
Inputs
Material Properties
Loading Conditions
Example studies:
Masouros, 2009, PhD Thesis, Imperial College
Masouros Knee Model
Intersegmental Finite Element Cadaveric Testing

## Slide 76: Finite Element Modelling
Outputs
Stress/Strain patterns
Glenoid cartilage
Intersegmental Finite Element Cadaveric Testing

## Slide 77: Finite Element Modelling
Uses
Estimating joint contact stress
  Improving implant design etc.
Simulating surgery
  Effects of meniscectomy, for example
Intersegmental Finite Element Cadaveric Testing

## Slide 78: Finite Element Modelling
30° flexion
Normal stresses in articular cartilage
Max. principal stresses in menisci
Masouros Knee Model
Intersegmental Finite Element Cadaveric Testing

## Slide 79: Finite Element Modelling
Intact
Meniscectomised
Meniscectomy results in:
Cartilage to cartilage contact
Less conformity
Decreased contact area
Increased contact stresses (up to 200%)1
Increased shear stresses
McDermott et al, 2008, Curr Orthop.
Intersegmental Finite Element Cadaveric Testing

## Slide 80: Modelling Limitations
Intersegmental Finite Element Cadaveric Testing
Intersegmental models
Every aspect of a model needs verification and validation
  Verification – internal consistency
  Validation – it represents the human body
BUT...purpose of a model is always to simulate what can’t be measured directly

## Slide 81: Modelling Limitations
Intersegmental Finite Element Cadaveric Testing
Motion capture: skin motion artifacts
Inverse dynamics: mass and inertial properties
Geometry: muscle modelling
Optimisation: relevant minimisation criteria

## Slide 82: Modelling Limitations
Intersegmental Finite Element Cadaveric Testing
Finite element models
Computing power
Material properties/equations
Boundary conditions/interfaces

## Slide 83: Modelling Summary
Experimental Data
Modelling
Mechanical Behaviour
Input
Validation
Clinical application
Output
Intersegmental Finite Element Cadaveric Testing

## Slide 84: Overall Summary
The human body and its structures are like any other solid object and obey Newton’s Laws of Motion
The human body can be simplified to allow investigation using basic mechanics and equations
Modelling is simply using these equations on a larger scale

## Slide 85: Suggested reading
General background
Principles of Mechanics and Biomechanics, Frank Bell, Stanley Thornes publishing
Lower-limb biomechanics and modelling
Clinical Gait Analysis, Chris Kirtley, Elsevier publishing. Particularly chapter 4: Biomechanics of Standing.